## Slide 1: Design of Digital Circuits Lecture 23a: More Caches
Prof. Onur Mutlu
ETH Zurich
Spring 2019
17 May 2019

## Slide 2: Readings
Caches
Required
  H&H Chapters 8.1-8.3
  Refresh: P&P Chapter 3.5
Recommended
  An early cache paper by Maurice Wilkes
    Wilkes, “Slave Memories and Dynamic Storage Allocation,” IEEE Trans. On Electronic Computers, 1965.

## Slide 3: Memory Hierarchy
Fundamental tradeoff
  Fast memory: small
  Large memory: slow
Idea: Memory hierarchy
Latency, cost, size,
bandwidth
CPU
Main
Memory
(DRAM)
RF
Cache
Hard Disk

## Slide 4: Cache
Generically, any structure that “memoizes” frequently used results to avoid repeating the long-latency operations required to reproduce the results from scratch, e.g. a web cache
Most commonly in the processor design context: an automatically-managed memory structure based on SRAM
  memoize in SRAM the most frequently accessed DRAM memory locations to avoid repeatedly paying for the DRAM access latency

## Slide 5: Caching Basics
Block (line): Unit of storage in the cache
  Memory is logically divided into cache blocks that map to locations in the cache
On a reference:
  HIT: If in cache, use cached data instead of accessing memory
  MISS: If not in cache, bring block into cache
    Maybe have to kick something else out to do it
Some important cache design decisions
  Placement: where and how to place/find a block in cache?
  Replacement: what data to remove to make room in cache?
  Granularity of management: large or small blocks? Subblocks?
  Write policy: what do we do about writes?
  Instructions/data: do we treat them separately?

## Slide 6: Cache Abstraction and Metrics
Cache hit rate = (# hits) / (# hits + # misses) = (# hits) / (# accesses)
Average memory access time (AMAT)
= ( hit-rate * hit-latency ) + ( miss-rate * miss-latency )
Aside: Is reducing AMAT always beneficial for performance?
Address
Tag Store
(is the address
in the cache?
+ bookkeeping)
Data Store
(stores
memory
blocks)
Hit/miss?
Data

## Slide 7: A Basic Hardware Cache Design
We will start with a basic hardware cache design
Then, we will examine a multitude of ideas to make it better

## Slide 8: Blocks and Addressing the Cache
Memory is logically divided into fixed-size blocks
Each block maps to a location in the cache, determined by the index bits in the address
  used to index into the tag and data stores
Cache access:
  1) index into the tag and data stores with index bits in address
  2) check valid bit in tag store
  3) compare tag bits in address with the stored tag in tag store
If a block is in the cache (cache hit), the stored tag should be valid and match the tag of the block
8-bit address
tag
index
byte in block
3 bits
3 bits
2b

## Slide 9: Direct-Mapped Cache: Placement and Access
Assume byte-addressable memory: 256 bytes, 8-byte blocks  32 blocks
Assume cache: 64 bytes, 8 blocks
  Direct-mapped: A block can go to only one location
  Addresses with same index contend for the same location
    Cause conflict misses
Tag store
Data store
Address
tag
index
byte in block
3 bits
3 bits
2b
V
tag
=?
MUX
byte in block
Hit?
Data
Block: 00000
Block: 00001
Block: 00010
Block: 00011
Block: 00100
Block: 00101
Block: 00110
Block: 00111
Block: 01000
Block: 01001
Block: 01010
Block: 01011
Block: 01100
Block: 01101
Block: 01110
Block: 01111
Block: 10000
Block: 10001
Block: 10010
Block: 10011
Block: 10100
Block: 10101
Block: 10110
Block: 10111
Block: 11000
Block: 11001
Block: 11010
Block: 11011
Block: 11100
Block: 11101
Block: 11110
Block: 11111
Main memory

## Slide 10: Direct-Mapped Caches
Direct-mapped cache: Two blocks in memory that map to the same index in the cache cannot be present in the cache at the same time
  One index  one entry
Can lead to 0% hit rate if more than one block accessed in an interleaved manner map to the same index
  Assume addresses A and B have the same index bits but different tag bits
  A, B, A, B, A, B, A, B, …  conflict in the cache index
  All accesses are conflict misses

## Slide 11: Set Associativity
Addresses 0 and 8 always conflict in direct mapped cache
Instead of having one column of 8, have 2 columns of 4 blocks
Tag store
Data store
V
tag
=?
V
tag
=?
Address
tag
index
byte in block
3 bits
2 bits
3b
Logic
MUX
MUX
byte in block
Key idea: Associative memory within the set
+ Accommodates conflicts better (fewer conflict misses)
-- More complex, slower access, larger tag store
SET
Hit?

## Slide 12: Higher Associativity
4-way
+ Likelihood of conflict misses even lower
-- More tag comparators and wider data mux; larger tags
Tag store
Data store
=?
=?
=?
=?
MUX
MUX
byte in block
Logic
Hit?

## Slide 13: Full Associativity
Fully associative cache
  A block can be placed in any cache location
Tag store
Data store
=?
=?
=?
=?
=?
=?
=?
=?
MUX
MUX
byte in block
Logic
Hit?

## Slide 14: Associativity (and Tradeoffs)
Degree of associativity: How many blocks can map to the same index (or set)?
Higher associativity
  ++ Higher hit rate
  -- Slower cache access time (hit latency and data access latency)
  -- More expensive hardware (more comparators)
Diminishing returns from higher
  associativity
associativity
hit rate

## Slide 15: Issues in Set-Associative Caches
Think of each block in a set having a “priority”
  Indicating how important it is to keep the block in the cache
Key issue: How do you determine/adjust block priorities?
There are three key decisions in a set:
  Insertion, promotion, eviction (replacement)
Insertion: What happens to priorities on a cache fill?
  Where to insert the incoming block, whether or not to insert the block
Promotion: What happens to priorities on a cache hit?
  Whether and how to change block priority
Eviction/replacement: What happens to priorities on a cache miss?
  Which block to evict and how to adjust priorities

## Slide 16: Eviction/Replacement Policy
Which block in the set to replace on a cache miss?
  Any invalid block first
  If all are valid, consult the replacement policy
    Random
    FIFO
    Least recently used (how to implement?)
    Not most recently used
    Least frequently used?
    Least costly to re-fetch?
      Why would memory accesses have different cost?
    Hybrid replacement policies
    Optimal replacement policy?

## Slide 17: Implementing LRU
Idea: Evict the least recently accessed block
Problem: Need to keep track of access ordering of blocks
Question: 2-way set associative cache:
  What do you need to implement LRU perfectly?
Question: 4-way set associative cache:
  What do you need to implement LRU perfectly?
  How many different orderings possible for the 4 blocks in the set?
  How many bits needed to encode the LRU order of a block?
  What is the logic needed to determine the LRU victim?

## Slide 18: Approximations of LRU
Most modern processors do not implement “true LRU” (also called “perfect LRU”) in highly-associative caches
Why?
  True LRU is complex
  LRU is an approximation to predict locality anyway (i.e., not the best possible cache management policy)
Examples:
  Not MRU (not most recently used)
  Hierarchical LRU: divide the N-way set into M “groups”, track the MRU group and the MRU way in each group
  Victim-NextVictim Replacement: Only keep track of the victim and the next victim

## Slide 19: Cache Replacement Policy: LRU or Random
LRU vs. Random: Which one is better?
  Example: 4-way cache, cyclic references to A, B, C, D, E
    0% hit rate with LRU policy
Set thrashing: When the “program working set” in a set is larger than set associativity
  Random replacement policy is better when thrashing occurs
In practice:
  Depends on workload
  Average hit rate of LRU and Random are similar
Best of both Worlds: Hybrid of LRU and Random
  How to choose between the two? Set sampling
    See Qureshi et al., “A Case for MLP-Aware Cache Replacement,“ ISCA 2006.

## Slide 20: What Is the Optimal Replacement Policy?
Belady’s OPT
  Replace the block that is going to be referenced furthest in the future by the program
  Belady, “A study of replacement algorithms for a virtual-storage computer,” IBM Systems Journal, 1966.
  How do we implement this? Simulate?
Is this optimal for minimizing miss rate?
Is this optimal for minimizing execution time?
  No. Cache miss latency/cost varies from block to block!
  Two reasons: Remote vs. local caches and miss overlapping
  Qureshi et al. “A Case for MLP-Aware Cache Replacement,“ ISCA 2006.

## Slide 21: Reading
Key observation: Some misses more costly than others as their latency is exposed as stall time. Reducing miss rate is not always good for performance. Cache replacement should take into account MLP of misses.
Moinuddin K. Qureshi, Daniel N. Lynch, Onur Mutlu, and Yale N. Patt, "A Case for MLP-Aware Cache Replacement" Proceedings of the 33rd International Symposium on Computer Architecture (ISCA), pages 167-177, Boston, MA, June 2006. Slides (ppt)

## Slide 22: Recall: Cache Structure
Address
Tag Store
(is the address
in the cache?
+ bookkeeping)
Data Store
(stores
memory
blocks)
Hit/miss?
Data

## Slide 23: Recall: Set Associativity
Addresses 0 and 8 always conflict in direct mapped cache
Instead of having one column of 8, have 2 columns of 4 blocks
Tag store
Data store
V
tag
=?
V
tag
=?
Address
tag
index
byte in block
3 bits
2 bits
3b
Logic
MUX
MUX
byte in block
Key idea: Associative memory within the set
+ Accommodates conflicts better (fewer conflict misses)
-- More complex, slower access, larger tag store
SET
Hit?

## Slide 24: What’s In A Tag Store Entry?
Valid bit
Tag
Replacement policy bits
Dirty bit?
  Write back vs. write through caches

## Slide 25: Handling Writes (I)
  When do we write the modified data in a cache to the next level?
    Write through: At the time the write happens
    Write back: When the block is evicted
  Write-back
    + Can combine multiple writes to the same block before eviction
      Potentially saves bandwidth between cache levels + saves energy
  -- Need a bit in the tag store indicating the block is “dirty/modified”
  Write-through
    + Simpler
    + All levels are up to date. Consistency: Simpler cache coherence because no need to check close-to-processor caches’ tag stores for presence
    -- More bandwidth intensive; no combining of writes

## Slide 26: Handling Writes (II)
Do we allocate a cache block on a write miss?
  Allocate on write miss: Yes
  No-allocate on write miss: No
Allocate on write miss
  + Can combine writes instead of writing each of them individually to next level
  + Simpler because write misses can be treated the same way as read misses
  -- Requires transfer of the whole cache block
No-allocate
  + Conserves cache space if locality of writes is low (potentially better cache hit rate)

## Slide 27: Handling Writes (III)
What if the processor writes to an entire block over a small amount of time?
Is there any need to bring the block into the cache from memory in the first place?
Why do we not simply write to only a portion of the block, i.e., subblock
  E.g., 4 bytes out of 64 bytes
  Problem: Valid and dirty bits are associated with the entire 64 bytes, not with each individual 4 bytes

## Slide 28: Subblocked (Sectored) Caches
Idea: Divide a block into subblocks (or sectors)
  Have separate valid and dirty bits for each subblock (sector)
  Allocate only a subblock (or a subset of subblocks) on a request
++ No need to transfer the entire cache block into the cache
(A write simply validates and updates a subblock)
++ More freedom in transferring subblocks into the cache (a cache block does not need to be in the cache fully)
  (How many subblocks do you transfer on a read?)
-- More complex design
-- May not exploit spatial locality fully
tag
subblock
v
subblock
v
subblock
v
d
d
d

## Slide 29: Instruction vs. Data Caches
Separate or Unified?
Pros and Cons of Unified:
  + Dynamic sharing of cache space: no overprovisioning that might happen with static partitioning (i.e., separate I and D caches)
  -- Instructions and data can thrash each other (i.e., no guaranteed space for either)
  -- I and D are accessed in different places in the pipeline. Where do we place the unified cache for fast access?
First level caches are almost always split
  Mainly for the last reason above
Higher level caches are almost always unified

## Slide 30: Multi-level Caching in a Pipelined Design
First-level caches (instruction and data)
  Decisions very much affected by cycle time
  Small, lower associativity; latency is critical
  Tag store and data store accessed in parallel
Second-level caches
  Decisions need to balance hit rate and access latency
  Usually large and highly associative; latency not as important
  Tag store and data store accessed serially
Serial vs. Parallel access of levels
  Serial: Second level cache accessed only if first-level misses
  Second level does not see the same accesses as the first
    First level acts as a filter (filters some temporal and spatial locality)
    Management policies are therefore different

## Slide 31: Cache Performance

## Slide 32: Cache Parameters vs. Miss/Hit Rate
Cache size
Block size
Associativity
Replacement policy
Insertion/Placement policy

## Slide 33: Cache Size
Cache size: total data (not including tag) capacity
  bigger can exploit temporal locality better
  not ALWAYS better
Too large a cache adversely affects hit and miss latency
  smaller is faster => bigger is slower
  access time may degrade critical path
Too small a cache
  doesn’t exploit temporal locality well
  useful data replaced often
Working set: the whole set of data the executing application references
  Within a time interval
hit rate
cache size
“working set”
size

## Slide 34: Block Size
Block size is the data that is associated with an address tag
  not necessarily the unit of transfer between hierarchies
    Sub-blocking: A block divided into multiple pieces (each w/ V/D bits)
Too small blocks
  don’t exploit spatial locality well
  have larger tag overhead
Too large blocks
  too few total # of blocks  less
    temporal locality exploitation
  waste of cache space and bandwidth/energy
  if spatial locality is not high
hit rate
block
size

## Slide 35: Large Blocks: Critical-Word and Subblocking
Large cache blocks can take a long time to fill into the cache
  fill cache line critical word first
  restart cache access before complete fill
Large cache blocks can waste bus bandwidth
  divide a block into subblocks
  associate separate valid and dirty bits for each subblock
  Recall: When is this useful?
tag
subblock
v
subblock
v
subblock
v
d
d
d

## Slide 36: Associativity
How many blocks can be present in the same index (i.e., set)?
Larger associativity
  lower miss rate (reduced conflicts)
  higher hit latency and area cost (plus diminishing returns)
Smaller associativity
  lower cost
  lower hit latency
    Especially important for L1 caches
Is power of 2 associativity required?
associativity
hit rate

## Slide 37: Classification of Cache Misses
Compulsory miss
  first reference to an address (block) always results in a miss
  subsequent references should hit unless the cache block is displaced for the reasons below
Capacity miss
  cache is too small to hold everything needed
  defined as the misses that would occur even in a fully-associative cache (with optimal replacement) of the same capacity
Conflict miss
  defined as any miss that is neither a compulsory nor a capacity miss

## Slide 38: How to Reduce Each Miss Type
Compulsory
  Caching cannot help
  Prefetching can: Anticipate which blocks will be needed soon
Conflict
  More associativity
  Other ways to get more associativity without making the cache associative
    Victim cache
    Better, randomized indexing
    Software hints?
Capacity
  Utilize cache space better: keep blocks that will be referenced
  Software management: divide working set and computation such that each “computation phase” fits in cache

## Slide 39: How to Improve Cache Performance
Three fundamental goals
Reducing miss rate
  Caveat: reducing miss rate can reduce performance if more costly-to-refetch blocks are evicted
Reducing miss latency or miss cost
Reducing hit latency or hit cost
The above three together affect performance

## Slide 40: Improving Basic Cache Performance
Reducing miss rate
  More associativity
  Alternatives/enhancements to associativity
    Victim caches, hashing, pseudo-associativity, skewed associativity
  Better replacement/insertion policies
  Software approaches
Reducing miss latency/cost
  Multi-level caches
  Critical word first
  Subblocking/sectoring
  Better replacement/insertion policies
  Non-blocking caches (multiple cache misses in parallel)
  Multiple accesses per cycle
  Software approaches

## Slide 41: Software Approaches for Higher Hit Rate
Restructuring data access patterns
Restructuring data layout
Loop interchange
Data structure separation/merging
Blocking
…

## Slide 42: Restructuring Data Access Patterns (I)
Idea: Restructure data layout or data access patterns
Example: If column-major
  x[i+1,j] follows x[i,j] in memory
  x[i,j+1] is far away from x[i,j]
This is called loop interchange
Other optimizations can also increase hit rate
  Loop fusion, array merging, …
Poor code
for i = 1, rows
for j = 1, columns
sum = sum + x[i,j]
  Better code
  for j = 1, columns
  for i = 1, rows
  sum = sum + x[i,j]

## Slide 43: Restructuring Data Access Patterns (II)
Blocking
  Divide loops operating on arrays into computation chunks so that each chunk can hold its data in the cache
  Avoids cache conflicts between different chunks of computation
  Essentially: Divide the working set so that each piece fits in the cache
Also called Tiling

## Slide 44: We did not cover the following slides. They are for your preparation for the next lecture.

## Slide 45: Restructuring Data Layout (I)
Pointer based traversal (e.g., of a linked list)
Assume a huge linked list (1B nodes) and unique keys
Why does the code on the left have poor cache hit rate?
  “Other fields” occupy most of the cache line even though rarely accessed!
struct Node {
struct Node* next;
int key;
char [256] name;
char [256] school;
}
while (node) {
if (nodekey == input-key) {
// access other fields of node
}
node = nodenext;
}

## Slide 46: Restructuring Data Layout (II)
Idea: separate frequently-used fields of a data structure and pack them into a separate data structure
Who should do this?
  Programmer
  Compiler
    Profiling vs. dynamic
  Hardware?
  Who can determine what is frequently used?
struct Node {
struct Node* next;
int key;
struct Node-data* node-data;
}
struct Node-data {
char [256] name;
char [256] school;
}
while (node) {
if (nodekey == input-key) {
// access nodenode-data
}
node = nodenext;
}

## Slide 47: Multi-Core Issues in Caching

## Slide 48: Caches in a Multi-Core System
CORE 1
L2 CACHE 0
SHARED L3 CACHE
DRAM INTERFACE
CORE 0
CORE 2
CORE 3
L2 CACHE 1
L2 CACHE 2
L2 CACHE 3
DRAM BANKS
DRAM MEMORY CONTROLLER

## Slide 49: Caches in Multi-Core Systems
Cache efficiency becomes even more important in a multi-core/multi-threaded system
  Memory bandwidth is at premium
  Cache space is a limited resource across cores/threads
How do we design the caches in a multi-core system?
Many decisions
  Shared vs. private caches
  How to maximize performance of the entire system?
  How to provide QoS to different threads in a shared cache?
  Should cache management algorithms be aware of threads?
  How should space be allocated to threads in a shared cache?

## Slide 50: Private vs. Shared Caches
Private cache: Cache belongs to one core (a shared block can be in multiple caches)
Shared cache: Cache is shared by multiple cores
CORE 0
CORE 1
CORE 2
CORE 3
L2
CACHE
L2
CACHE
L2
CACHE
DRAM MEMORY CONTROLLER
L2
CACHE
CORE 0
CORE 1
CORE 2
CORE 3
DRAM MEMORY CONTROLLER
L2
CACHE

## Slide 51: Resource Sharing Concept and Advantages
Idea: Instead of dedicating a hardware resource to a hardware context, allow multiple contexts to use it
  Example resources: functional units, pipeline, caches, buses, memory
Why?
+ Resource sharing improves utilization/efficiency  throughput
  When a resource is left idle by one thread, another thread can use it; no need to replicate shared data
+ Reduces communication latency
  For example, data shared between multiple threads can be kept in the same cache in multithreaded processors
+ Compatible with the shared memory programming model

## Slide 52: Resource Sharing Disadvantages
Resource sharing results in contention for resources
  When the resource is not idle, another thread cannot use it
  If space is occupied by one thread, another thread needs to re-occupy it
- Sometimes reduces each or some thread’s performance
- Thread performance can be worse than when it is run alone
- Eliminates performance isolation  inconsistent performance across runs
- Thread performance depends on co-executing threads
- Uncontrolled (free-for-all) sharing degrades QoS
- Causes unfairness, starvation
Need to efficiently and fairly utilize shared resources

## Slide 53: Private vs. Shared Caches
Private cache: Cache belongs to one core (a shared block can be in multiple caches)
Shared cache: Cache is shared by multiple cores
CORE 0
CORE 1
CORE 2
CORE 3
L2
CACHE
L2
CACHE
L2
CACHE
DRAM MEMORY CONTROLLER
L2
CACHE
CORE 0
CORE 1
CORE 2
CORE 3
DRAM MEMORY CONTROLLER
L2
CACHE

## Slide 54: Shared Caches Between Cores
Advantages:
  High effective capacity
  Dynamic partitioning of available cache space
    No fragmentation due to static partitioning
    If one core does not utilize some space, another core can
  Easier to maintain coherence (a cache block is in a single location)
Disadvantages
  Slower access (cache not tightly coupled with the core)
  Cores incur conflict misses due to other cores’ accesses
    Misses due to inter-core interference
    Some cores can destroy the hit rate of other cores
  Guaranteeing a minimum level of service (or fairness) to each core is harder (how much space, how much bandwidth?)

## Slide 55: Cache Coherence

## Slide 56: Cache Coherence
Basic question: If multiple processors cache the same block, how do they ensure they all see a consistent state?
P1
P2
x
Interconnection Network
Main Memory
1000

## Slide 57: The Cache Coherence Problem
P1
P2
x
Interconnection Network
Main Memory
ld r2, x
1000
1000

## Slide 58: The Cache Coherence Problem
P1
P2
x
Interconnection Network
Main Memory
ld r2, x
ld r2, x
1000
1000
1000

## Slide 59: The Cache Coherence Problem
P1
P2
x
Interconnection Network
Main Memory
ld r2, x
add r1, r2, r4
st x, r1
ld r2, x
1000
1000
2000

## Slide 60: The Cache Coherence Problem
P1
P2
x
Interconnection Network
Main Memory
ld r2, x
add r1, r2, r4
st x, r1
ld r2, x
1000
1000
2000
ld r5, x
Should NOT load 1000

## Slide 61: Cache Examples: For You to Study

## Slide 62: Cache Terminology
Capacity (C):
  the number of data bytes a cache stores
Block size (b):
  bytes of data brought into cache at once
Number of blocks (B = C/b):
  number of blocks in cache: B = C/b
Degree of associativity (N):
  number of blocks in a set
Number of sets (S = B/N):
  each memory address maps to exactly one cache set

## Slide 63: How is data found?
Cache organized into S sets
Each memory address maps to exactly one set
Caches categorized by number of blocks in a set:
  Direct mapped: 1 block per set
  N-way set associative: N blocks per set
  Fully associative: all cache blocks are in a single set
Examine each organization for a cache with:
  Capacity (C = 8 words)
  Block size (b = 1 word)
  So, number of blocks (B = 8)

## Slide 64: Direct Mapped Cache

## Slide 65: Direct Mapped Cache Hardware

## Slide 66: Direct Mapped Cache Performance
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0xC($0)
lw $t3, 0x8($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate =
66

## Slide 67: Direct Mapped Cache Performance
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0xC($0)
lw $t3, 0x8($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = 3/15 = 20%
Temporal Locality Compulsory Misses
67

## Slide 68: Direct Mapped Cache: Conflict
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0x24($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate =
68

## Slide 69: Direct Mapped Cache: Conflict
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0x24($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = 10/10 = 100%
Conflict Misses
69

## Slide 70: N-Way Set Associative Cache

## Slide 71: N-way Set Associative Performance
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0x24($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate =
71

## Slide 72: N-way Set Associative Performance
# MIPS assembly code
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0x24($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = 2/10
= 20%
Associativity reduces conflict misses
72

## Slide 73: Fully Associative Cache
No conflict misses
Expensive to build
73

## Slide 74: Spatial Locality?
Increase block size:
  Block size, b = 4 words
  C = 8 words
  Direct mapped (1 block per set)
  Number of blocks, B = C/b = 8/4 = 2
74

## Slide 75: Direct Mapped Cache Performance
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0xC($0)
lw $t3, 0x8($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate =
75

## Slide 76: Direct Mapped Cache Performance
addi $t0, $0, 5
loop: beq $t0, $0, done
lw $t1, 0x4($0)
lw $t2, 0xC($0)
lw $t3, 0x8($0)
addi $t0, $t0, -1
j loop
done:
Miss Rate = 1/15
= 6.67%
Larger blocks reduce compulsory misses through spatial locality
76

## Slide 77: Cache Organization Recap
Main Parameters
  Capacity: C
  Block size: b
  Number of blocks in cache: B = C/b
  Number of blocks in a set: N
  Number of Sets: S = B/N
Organization | Number of Ways (N) | Number of Sets (S = B/N)
Direct Mapped | 1 | B
N-Way Set Associative | 1 < N < B | B / N
Fully Associative | B | 1
77

## Slide 78: Capacity Misses
Cache is too small to hold all data of interest at one time
  If the cache is full and program tries to access data X that is not in cache, cache must evict data Y to make room for X
  Capacity miss occurs if program then tries to access Y again
  X will be placed in a particular set based on its address
In a direct mapped cache, there is only one place to put X
In an associative cache, there are multiple ways where X could go in the set.
How to choose Y to minimize chance of needing it again?
  Least recently used (LRU) replacement: the least recently used block in a set is evicted when the cache is full.

## Slide 79: Types of Misses
Compulsory: first time data is accessed
Capacity: cache too small to hold all data of interest
Conflict: data of interest maps to same location in cache
Miss penalty: time it takes to retrieve a block from lower level of hierarchy

## Slide 80: LRU Replacement
# MIPS assembly
lw $t0, 0x04($0)
lw $t1, 0x24($0)
lw $t2, 0x54($0)
80

## Slide 81: LRU Replacement
# MIPS assembly
lw $t0, 0x04($0)
lw $t1, 0x24($0)
lw $t2, 0x54($0)
81